CAN Module Design Document
- Comgen - CAN -
DXXXXXX

Primary Author(s):	Carlos Calvillo Cortes
Version:	0.1
Maturity:	draft
Project:	calvos
Document ID:	DXXXXXX
Additional Information:

# Document History
Version	Date (dd/Mmm/yyyy)	Author(s)	Description
0.1	11/Jan/2021	Carlos Calvillo Cortes	Initial draft version

# Document Overview
This is a design document for the CAN module of the comgen package.
# CAN module
## Functions
## Data structures
### Class “SignalAccess”
Class SignalAccess is used to model an abstract access to a signal. The access can be read or write access depending on the consumer of the object’s of this class.
#### Class “PieceAccess”
Models a piece of access for the signal in the parent’s SignalAccess class. A piece here refers to a string that is OR’ed to form a whole C string for accessing the given signal with the specified layout.
Members of this class are described below.

DATA
OP₁
T₁
M₁
S₁
OP₂
M₂
S₂
T₂
M₃

Above elements will form a string with following format:
( T₂ )( ( ( ( *( T₁ * )(DATA) & M₁ ) OP₁ S₁ ) & M₂ ) OP₂ S₂ ) & M₃
DATA: The name of the data to be accessed shall be a pointer variable. Examples:
- my_array
- &my_array[0]
- &my_array[5]
T₁: Type casting 1. Will cast the type given by DATA. Shall be any valid basic C data type in the SW. Examples:
- usigned int
- usigned long long int
- uint32_t (provided that uint32_t is defined as a corresponding data type, .e.g., “typedef unsigned int uint32_t;”)
T₂: Type casting 2.
M₁: Mask 1. Will mask out (‘and’ operator ‘&’) non relevant bits of the variable DATA. Shall have same lenght of the casting type T₁. For example if T₁ casts to a 16-bit data, then the mask shall be of 16 bits, etc. Examples:
- 0x1Fu (will mask out the 3 most significant bits in a 8-bit variable)
- 0x0FFFu (will mask out the 4 most significant bits in a 16-bit variable)
OP₁: Shifting operator 1. Can be left shifting (<<) or right shifting (>>) as required.
S₁: Shifting bits 1. Number of bits to shift following shifting operator OP₁.
M₂: Mask 2.
OP₂: Shifting operator 2.
S₂: Shifting bits 2.