## Slide 1: Introduction to CAN protocol
Carlos Calvillo
November 2022 / v1.1

## Slide 2: Contents
  CAN Overview
  Protocol Specification
      Physical Layer
      Data Frame Format
      Remote Frame Format
      Arbitration
      Bit Stuffing
      Error Handling
  Network Design
      Transmission Types
      Design Steps

## Slide 3: Contents
  CAN Overview
  Protocol Specification
      Physical Layer
      Data Frame Format
      Remote Frame Format
      Arbitration
      Bit Stuffing
      Error Handling
  Network Design
      Transmission Types
      Design Steps

## Slide 4: CAN Overview
CAN stands for “Controller Area Network”
  Asynchronous serial communication protocol
  Efficient support for distributed real-time control systems
  High reliability
  Bit-rates:
    Classic CAN  Up to 1 Mbit/s
    CAN FD  Up to 5 Mbit/s

## Slide 5: CAN Overview
CAN stands for “Controller Area Network”
  Asynchronous serial communication protocol
  Efficient support for distributed real-time control systems
  High reliability
  Bit-rates:
    Classic CAN  Up to 1 Mbit/s
    CAN FD  Up to 5 Mbit/s
Focus in this presentation

## Slide 6: CAN Overview

## Slide 7: CAN Overview
Brief CAN history
1987: First CAN controller chips (Intel 82526, Philips 82C200)
1993: CAN is standardized in ISO 11898
2015: The CAN FD protocol is standardized within ISO 11898
1986: Bosch develops CAN protocol as a solution to traditional wiring
1991: Bosch specification CAN 2.0 (CAN 2.0A: 11 bit, 2.0B: 29 bit)
2012: Bosch released the CAN FD 1.0
2016: The physical CAN layer for data-rates up to 5 Mbit/s standardized in ISO 11898-2
time

## Slide 8: CAN Overview

## Slide 9: CAN Overview
CAN in context with other protocols used in automotive

## Slide 10: CAN Overview
CAN for distributed architectures
  Bus network topology
  Good bandwidth for control-oriented applications
  Multi-master protocol
  Deterministic communication
  Hot-in-out of nodes in network (no need for restarting the network)
  Cost efficient

## Slide 11: CAN Overview
CAN Network classifications
  Low speed
    83.3 kbit/s, 125 kbit/s
    Two-wire or single-wire bus possible (SAE J2422)
    Common in early vehicles using CAN
  High speed
    250 kbit/s, 500 kbit/s, 1 Mbit/s
    Two-wire bus
    Most used in modern vehicles

## Slide 12: CAN Overview
CAN Network classifications
  Low speed
    83.3 kbit/s, 125 kbit/s
    Two-wire or single-wire bus possible (SAE J2422)
    Common in early vehicles using CAN
  High speed
    250 kbit/s, 500 kbit/s, 1 Mbit/s
    Two-wire bus
    Most used in modern vehicles
Focus in this presentation

## Slide 13: CAN Overview
Typical vehicle has multiple CAN networks
  Networks for powertrain, telematics, body control, etc.
  Each network with multiple ECUs (Electronic Control Units)
  “Gateway” ECU:
    Provides interconnection between different CAN networks
      By transporting messages from one network to another…
    Provides connectivity to external diagnostic tools (e.g., via OBD connector).

## Slide 14: CAN Overview

## Slide 15: CAN Overview
~80% of CAN applications are in automotive industry; however, CAN is also used in other application areas:
  Agricultural Vehicles
  Medical Equipment
  Robotics
  Industrial Applications, etc.

## Slide 16: Contents
  CAN Overview
  Protocol Specification
      Physical Layer
      Data Frame Format
      Remote Frame Format
      Arbitration
      Bit Stuffing
      Error Handling
  Network Design
      Transmission Types
      Design Steps

## Slide 17: Protocol Specification
CAN uses Non-Return-to-Zero (NRZ) bit coding
  Bus level is kept constant for each bit-time (no transition within a single bit)
  Less transitions (as compared to other bit codings)  higher bandwidth
  Reduced electro-magnetic emissions
  Receiver may lose synchronization with long sequence of bits with same value
   Bit-stuffing technique mitigates this situation

## Slide 18: Protocol Specification
Physical Layer
  Differential voltage transmission (two-wires)
    CAN High (CAN-H), CAN Low (CAN-L)
    Reference to common GND
  Unshielded Twisted Pair
  Termination resistor at each end of the CAN Bus  120 Ω
    Allow power dissipation for generation of “recessive” levels
    Prevent reflections
  Line resistance: less than 60 Ω

## Slide 19: Protocol Specification
Physical Layer
Notes: High speed:
- Dominant  Difference greater or equal than 0.9V
- Recessive  Difference greater or smaller than 0.5V

## Slide 20: Protocol Specification
Physical Layer
  CAN Bus Length
Bit Rate | Max. recommended bus length
50 kbit/s | 1000 m
125 kbit/s | 500 m
250 kbit/s | 200 m
500 kbit/s | 100 m
1 Mbit/s | 40 m

## Slide 21: Protocol Specification
CAN Transceiver, CAN Controller, CAN Host

## Slide 22: Protocol Specification
CAN transceiver
  Allows connection of node (ECU) to the CAN bus
  Interfaces between CAN bus voltage levels (CAN-H and CAN-L) and CAN controller voltage levels (e.g., RXD and TXD pins at TTL voltage levels).

## Slide 23: Protocol Specification
CAN controller
  HW device that handles the CAN messages  decodes the CAN protocol
  Can be a standalone device, e.g.:
    Microchip MCP2515 (SPI interface with Host MCU)
  Can be integrated in the host MCU as a peripheral , e.g.:
    NXP FlexCAN peripheral
    Infineon MultiCAN peripheral

## Slide 24: Protocol Specification
CAN host
  Device that host the application (an MCU, a computer)
  Consumes the CAN messages and uses their conveyed signals
  Generates and packs signals into CAN messages for subsequent transmission in the CAN bus

## Slide 25: Protocol Specification
RT = Termination Resistor
In this example, each participant ECU is a network node.
It is possible that a single ECU implements multiple nodes (each with its own transceiver and controller channels).

## Slide 26: Protocol Specification
Abstraction
Transceiver abstraction
CAN Transceiver
(From Microchip MCP2551)

## Slide 27: Protocol Specification
CAN Transceiver
(From Microchip MCP2551)
Transceiver abstraction
Bus goes to dominant level when “switch” closes
Abstraction

## Slide 28: Protocol Specification
Note: This is just an abstraction used for illustrating the dominant and recessive levels behavior. Not intended to show actual circuitry of physical layer

## Slide 29: Protocol Specification
Recessive bus level
  Logical one is known as recessive level
  When bus is idle, it shall be in recessive level
Dominant bus level
  Logical zero is known as dominant level
  If any node publishes a dominant value, the whole bus goes to dominant level even if another node is publishing a recessive value at the same time

## Slide 30: Protocol Specification
Communication Principle
  Carrier-sense, multiple-access with collision detection (CSMA/CD)
    Carrier-sense: all CAN nodes are sensing the bus, e.g., to see if it is idle
    Multiple-access: CAN is a multi-master protocol, i.e., any node can start transmission if bus is idle
    Collision detection:
      CAN defines an arbitration technique for detecting collisions when multiple nodes attempt to publish a frame at the same time
      Non-destructive arbitration: In case of collision, one node always wins the arbitration and can publish its frame

## Slide 31: Protocol Specification
Communication Principle
  Message based communication
    Data signals are packed into messages (for now message = frame)
    Message can carry from 0 to 8 data bytes (single frame)
    Unique identifier (ID) is defined for each message
      ID can be of 11 bits (standard) or 29 bits (extended)
    Direction of data transfer is defined (fixed) per each message:
      Each message shall have only one publisher node (transmitter).
      Each message can be assigned to one or more subscriber nodes (receivers)

## Slide 32: Protocol Specification
Communication Principle
  Signals are “packed” into messages, example:
Byte 0
Byte 1
Byte 2
Byte 3
Byte 4
Byte 5
Byte 6
Byte 7
Signal: vehicle_speed
Bit size: 8
Units: km/h
Range: 0 – 255 km/h
Layout: Byte 0, Bit 0
Signal: shift_gear
Bit size: 3
Enumeration: Park, Reverse, Neutral, Drive, L1, L2, SNA
Layout: Byte 2, Bit 1
Signal: error_flag
Bit size: 1
Units: boolean
Layout: Byte 7, Bit 7
MSB
LSB
CAN Message ID: 0x145
MSB
LSB
MSB
LSB
Message Data

## Slide 33: Protocol Specification
Communication Principle
  Example of “Message matrix”
Message Name | Message ID | Publisher Node | Subscriber(s) node(s)
BCM_MSG1 | 0x145 | BCM | ABS, DCU
BCM_MSG2 | 0x150 | BCM | DCU
ABS_MSG1 | 0x020 | ABS | BCM
DCU_MSG1 | 0x210 | DCU | BCM, ABS
DCU_MSG2 | 0x213 | DCU | BCM
BCM
ABS
DCU
CAN Bus

## Slide 34: Protocol Specification
Communication Principle
  Acceptance Filters
    All nodes are “capable” of seeing all published messages, however, that doesn’t mean that all messages are of interest for all nodes.
    CAN controllers are capable of filtering messages not subscribed by the node to reduce SW CPU load.
      Acceptance filters by HW may filter by individual IDs, ranges of IDs, ID masks, etc.
      Additional SW filtering performed if HW filtering didn’t reject 100% of non-subscribed messages.

## Slide 35: Protocol Specification
CAN Frame
  Frames are the basic units of transmission/reception in CAN protocol
  CAN defines different frame formats to convey data, errors, etc.
  Data is transmitted in Data Frames

## Slide 36: Protocol Specification
Classic CAN Frame Types
Standard Data Frame
Extended Data Frame
Standard Remote Frame
Extended Remote Frame
Active Error Frame
Passive Error Frame
Data Frame
Remote Frame
Error Frame
Overload Frame

## Slide 37: Protocol Specification
Classic CAN Frame Types
Standard Data Frame
Extended Data Frame
Standard Remote Frame
Extended Remote Frame
Active Error Frame
Passive Error Frame
Data Frame
Remote Frame
Error Frame
Overload Frame

## Slide 38: Data Frame Format
Data Frame
  Frames intended for publishing data
  Most used frames in CAN networks
  Two variants:
    Standard Data Frame  11-bit message identifier
    Extended Data Frame  29-bit message identifier

## Slide 39: Data Frame Format
Data Frame Fields:
  Start-of-Frame (SOF)
  Arbitration
  Control
  Data
  CRC
  Acknowledge (ACK)
  End-of-Frame (EOF)
Inter-Frame Space: Mandatory space between subsequent frames
Bus IDLE: bus is considered idle if at least 11 bits with recessive value are observed

## Slide 40: Data Frame Format
Start-of-Frame (SOF)
  Single bit with dominant level
  Indicates the beginning of a new frame

## Slide 41: Data Frame Format
Standard Format  Message identifier of 11 bits (211 different messages)
Extended Format  Message identifier of 29 bits (229 different messages)

## Slide 42: Data Frame Format
Identifier: Used to uniquely identify each message in the network
  11-bits for standard format frames
Remote Transmission Request (RTR): 1-bit; indicates if current frame is a data frame (provides data) or a remote frame (requests data)
  Dominant value for data frames
  Recessive value for remote frames

## Slide 43: Data Frame Format
Identifier: 29-bits for extended format frames.
  Formed by the Base Identifier of 11 bits (most-significant bits of the ID) plus the Extended identifier of 18 bits (least-significant bits of the ID).
Identifier Extension bit (IDE): 1-bit; Indicates if current frame is a standard frame (dominant value) or an extended frame (recessive value).

## Slide 44: Data Frame Format
Substitute Remote Request (SRR): 1-bit. Only applicable for extended format. Substitutes the position of the RTR bit in standard format.
  Transmitted always with recessive value in extended format
  Allows Standard Frames to have higher priority than Extended Frames with same Base identifier values.
RTR: Same meaning as in standard format but located after the “extended identifier” field.

## Slide 45: Data Frame Format
IDE: In standard format, the IDE bit is part of the “Control Field”. Same meaning as before  Indicates if current frame is a standard frame (dominant value) or an extended frame (recessive value).
r1: In extended format, this is a reserved bit not being used. Transmitted with dominant value.
r0: Reserved bit not being used. Transmitted with dominant value.

## Slide 46: Data Frame Format
DLC (Data Length Code): 4-bits. Indicates how many data bytes are conveyed in this frame.
  From 0 to 8 bytes max.
  Assumed max of 8 data bytes even if DLC value is higher than 8.

## Slide 47: Data Frame Format
Data Field
  From 0 to max. 8 data bytes
  Number of data bytes depend on value of DLC
  Most-significant-bit transmitted first, Least-significant-bit last.

## Slide 48: Data Frame Format
Cyclic Redundancy Check (CRC) sequence: 15-bits. Used for error detection during the transfer of a Frame.
  CRC calculation uses fields SOF, Arbitration Field, Control Field and Data Field (if present)
  CRC is calculated without stuffing bits
  Receiver node validates the received bit stream using the received CRC
  In case of CRC fail, the data in the frame is discarded

## Slide 49: Data Frame Format
CRC delimiter: 1-bit.
  Signals the end of the CRC field
  A single bit with recessive value

## Slide 50: Data Frame Format
Acknowledge (ACK) bit: Indicates if at least one node correctly received the frame
  Transmitted with recessive value by the publisher
  Any node shall overwrite this bit to dominant value if the frame was received correctly including CRC check (before acceptance filter of receivers)

## Slide 51: Data Frame Format
Acknowledge (ACK) bit
  If publisher sees this bit with recessive value, it may mean that:
    Frame had an error during the transmission and, hence, no other node acknowledged it, or,
    There is no other node connected to the network

## Slide 52: Data Frame Format
ACK delimiter:
  Signals the end of the Acknowledge field
  A single bit with recessive value

## Slide 53: Data Frame Format
End-of-Frame (EOF): 7-bits.
  Signals the end of the frame
  7 bits with recessive level

## Slide 54: Data Frame Format
Intermission field:
  3 recessive bits
  During intermission, no transmission of data or remote frames is allowed

## Slide 55: Data Frame Format
Suspend transmission field:
  Only generated by nodes in “passive error” state and associated to their own frame transmissions
  8 recessive bits

## Slide 56: Data Frame Format
Bus idle
  Bus is available for nodes to begin transmission of frames
  Arbitrary length

## Slide 57: Protocol Specification
Classic CAN Frame Types
Standard Data Frame
Extended Data Frame
Standard Remote Frame
Extended Remote Frame
Active Error Frame
Passive Error Frame
Data Frame
Remote Frame
Error Frame
Overload Frame

## Slide 58: Remote Frame Format
Purpose of a Remote Frame is to ask for data rather than to publish it as in the case of a Data Frame.
A node can ask for a given message to be transmitted by its publisher by generating a Remote Frame with ID equal to the Data Frame ID being requested
When a node sees a Remote Frame asking for an ID which it owns, the node shall start transmission of the corresponding Data Frame as soon as possible.

## Slide 59: Remote Frame Format
Remote Frame format is very similar to the format of a Data Frame  It contains all fields of a Data frame except for the “Data Field”
Remote Frame can also have standard or extended formats analogue to those of Data Frames
A Remote Frame is distinguished from a Data Frame by the RTR bit being recessive.

## Slide 60: Remote Frame Format

## Slide 61: Frame arbitration
The last part of a Data or Remote frame consists of at least 11 recessive bits
  ACK delimiter (1-bit) + EOF (7-bits) + Intermission field (3-bits) = 11 bits
During normal transmission of a Data or Remote frame, the bus shall never have 11 consecutive recessive bits (due to bit stuffing)
Therefore, nodes can consider bus as being idle after seeing 11 consecutive recessive bits

## Slide 62: Frame arbitration
Scenario
  A Data Frame is currently being transmitted by Node A
  3 nodes (Node B, Node C and Node D) are waiting for the bus to become idle in order to begin Data Frame transmission
    Waiting to see 11 consecutive recessive bits
  The 3 nodes see the bus in idle at the same time and they start publishing their Data Frames
  A collision occurs since multiple nodes are trying to publish different messages in the bus at the same time!

## Slide 63: Frame arbitration
CAN Message Arbitration
  CAN provides a non-destructive message arbitration mechanism
  At least one node competing from the bus will win the bus arbitration and complete its frame transmission
  Loser nodes will wait for the next time the bus is idle in order to attempt their Frame transmissions
     Typically, CAN controllers manage automatic re-transmission attempts

## Slide 64: Frame arbitration
CAN Message Arbitration
  CAN message arbitration occurs during the publication of the “Arbitration Field”, in particular during the publication of the “Frame Identifier”.
   The message Identifier is at the center of the arbitration criteria
  Frame Identifier is transmitted bit by bit starting with the Most-Significant one.
  During transmission of the “Identifier Field”, CAN nodes transmit each bit and read it back to verify the actual bus level for that bit

## Slide 65: Frame arbitration
CAN Message Arbitration
  If the read back bit level from the bus corresponds to the transmitted one, then arbitration has not been lost and the Node proceeds with the transmission of the next identifier bit
     If a Node can publish all the Frame identifier bits, then it has won the bus arbitration and can proceed with the rest of the Frame transmission!
  If the read back bit level from the bus is opposite to the transmitted one, then arbitration has been lost.
    The node shall stop transmission of further bits of the Frame

## Slide 66: Frame arbitration
CAN Message Arbitration
  Bit differences between transmitted bit levels and actual bus levels can be due to a node publishing a “dominant” level against “recessive” levels from other nodes
Arbitration Example
  Node B wants to transmit message 0x35
  Node C wants to transmit message 0x26
  Node D wants to transmit message 0x343
At the same time!

## Slide 67: Frame arbitration
Arbitration Example
0
0
0
0
0
1
1
0
1
0
1
0
SOF
Identifier (11-bits)
Node B
Msg 0x35
0
0
0
0
0
1
0
0
1
1
0
0
Node C
Msg 0x26
0
1
1
0
1
0
0
0
0
1
1
0
Node D
Msg 0x343

## Slide 68: Frame arbitration
Arbitration Example
0
0
1
0
0
1
1
0
1
0
1
0
SOF
Identifier (11-bits)
Node B
Msg 0x35
0
0
0
0
0
1
0
0
1
1
0
0
Node C
Msg 0x26
0
1
1
0
1
0
0
0
0
1
1
0
Node D
Msg 0x343
Actual
Bus Level
0
0
1
0
0
1
1
0
1
0
1
0
All nodes see the bus idle at the same time and start frame transmission

## Slide 69: Frame arbitration
Arbitration Example
0
0
1
0
0
1
1
0
1
0
1
0
SOF
Identifier (11-bits)
Node B
Msg 0x35
0
0
0
0
0
1
0
0
1
1
0
0
Node C
Msg 0x26
0
1
1
0
1
0
0
0
0
1
1
0
Node D
Msg 0x343
Actual
Bus Level
0
0
1
0
0
1
1
0
1
0
1
0
Nodes start publishing their frame IDs and compare transmitted bits against actual bus level

## Slide 70: Frame arbitration
Arbitration Example
0
0
0
0
0
1
1
0
1
0
1
0
SOF
Identifier (11-bits)
Node B
Msg 0x35
0
0
0
0
0
1
0
0
1
1
0
0
Node C
Msg 0x26
0
1
1
0
1
0
0
0
0
1
1
0
Node D
Msg 0x343
Actual
Bus Level
0
0
0
0
0
1
0
0
1
1
0
0

## Slide 71: Frame arbitration
Arbitration Example
0
0
0
0
0
1
1
0
1
0
1
0
SOF
Identifier (11-bits)
Node B
Msg 0x35
0
0
0
0
0
1
0
0
1
1
0
0
Node C
Msg 0x26
0
1
1
0
1
0
0
0
0
1
1
0
Node D
Msg 0x343
Actual
Bus Level
0
0
0
0
0
1
0
0
1
1
0
0
Node D has lost arbitration!

## Slide 72: Frame arbitration
Arbitration Example
0
0
0
0
0
1
1
0
1
0
1
0
SOF
Identifier (11-bits)
Node B
Msg 0x35
0
0
0
0
0
1
0
0
1
1
0
0
Node C
Msg 0x26
0
1
1
0
1
0
0
0
0
1
1
0
Node D
Msg 0x343
Actual
Bus Level
0
0
0
0
0
1
0
0
1
1
0
0

## Slide 73: Frame arbitration
Arbitration Example
0
0
0
0
0
1
1
0
1
0
1
0
SOF
Identifier (11-bits)
Node B
Msg 0x35
0
0
0
0
0
1
0
0
1
1
0
0
Node C
Msg 0x26
0
1
1
0
1
0
0
0
0
1
1
0
Node D
Msg 0x343
Actual
Bus Level
0
0
0
0
0
1
0
0
1
1
0
0

## Slide 74: Frame arbitration
Arbitration Example
0
0
0
0
0
1
1
0
1
0
1
0
SOF
Identifier (11-bits)
Node B
Msg 0x35
0
0
0
0
0
1
0
0
1
1
0
0
Node C
Msg 0x26
0
1
1
0
1
0
0
0
0
1
1
0
Node D
Msg 0x343
Actual
Bus Level
0
0
0
0
0
1
0
0
1
1
0
0

## Slide 75: Frame arbitration
Arbitration Example
0
0
0
0
0
1
1
0
1
0
1
0
SOF
Identifier (11-bits)
Node B
Msg 0x35
0
0
0
0
0
1
0
0
1
1
0
0
Node C
Msg 0x26
0
1
1
0
1
0
0
0
0
1
1
0
Node D
Msg 0x343
Actual
Bus Level
0
0
0
0
0
1
0
0
1
1
0
0

## Slide 76: Frame arbitration
Arbitration Example
0
0
0
0
0
1
1
0
1
0
1
0
SOF
Identifier (11-bits)
Node B
Msg 0x35
0
0
0
0
0
1
0
0
1
1
0
0
Node C
Msg 0x26
0
1
1
0
1
0
0
0
0
1
1
0
Node D
Msg 0x343
Actual
Bus Level
0
0
0
0
0
1
0
0
1
1
0
0

## Slide 77: Frame arbitration
Arbitration Example
0
0
0
0
0
1
1
0
1
0
1
0
SOF
Identifier (11-bits)
Node B
Msg 0x35
0
0
0
0
0
1
0
0
1
1
0
0
Node C
Msg 0x26
0
1
1
0
1
0
0
0
0
1
1
0
Node D
Msg 0x343
Actual
Bus Level
0
0
0
0
0
1
0
0
1
1
0
0
Node B has lost arbitration!

## Slide 78: Frame arbitration
Arbitration Example
0
0
0
0
0
1
1
0
1
0
1
0
SOF
Identifier (11-bits)
Node B
Msg 0x35
0
0
0
0
0
1
0
0
1
1
0
0
Node C
Msg 0x26
0
1
1
0
1
0
0
0
0
1
1
0
Node D
Msg 0x343
Actual
Bus Level
0
0
0
0
0
1
0
0
1
1
0
0

## Slide 79: Frame arbitration
Arbitration Example
0
0
0
0
0
1
1
0
1
0
1
0
SOF
Identifier (11-bits)
Node B
Msg 0x35
0
0
0
0
0
1
0
0
1
1
0
0
Node C
Msg 0x26
0
1
1
0
1
0
0
0
0
1
1
0
Node D
Msg 0x343
Actual
Bus Level
0
0
0
0
0
1
0
0
1
1
0
0
Node C wins arbitration!

## Slide 80: Frame arbitration
CAN Message Arbitration
  Critical data shall be transmitted in messages with low ID value
The lower the ID value the higher the priority!

## Slide 81: Bit Stuffing
CAN provides a technique to overcome the problem of lost synchronization due to its asynchronous nature and its NRZ bit codification
   Bit Stuffing technique

## Slide 82: Bit Stuffing
Bit Stuffing technique:
  Never allow more than 5 bits with the same level during Data or Remote Frame transmission
  Each time 5 bits with same level are observed in the bus, a bit (known as stuffing bit) shall be inserted with opposite level.
    This ensure edges at least every 5 bits
    Edges are opportunities for re-synchronization of nodes
  The 5 bits count shall also include the inserted stuffing bits

## Slide 83: Bit Stuffing
Bit Stuffing technique:
  Bit stuffing applies from Start-of-Frame up to and including the CRC sequence field
  CRC calculations are done without stuffing bits (after de-stuffing from receiver side)

## Slide 84: Bit Stuffing
Bit Stuffing example 1:
0
1
1
0
0
0
0
0
1
0
Original Bit Stream Sequence
Bit Stream Sequence with stuffing bits
Stuff
bit
0
1
1
0
0
0
0
0
1
1
0

## Slide 85: Bit Stuffing
Bit Stuffing example 2:
0
0
0
0
0
0
1
1
1
1
Original Bit Stream Sequence
Bit Stream Sequence with stuffing bits
Stuff
bit
0
0
0
0
0
1
0
1
1
1
1
1
1
1
0
1
Stuff
bit

## Slide 86: Bit Stuffing
Bit Stuffing example 3:
0
0
0
0
0
1
1
1
1
0
Original Bit Stream Sequence
Bit Stream Sequence with stuffing bits
Stuff
bit
0
0
0
0
0
1
1
1
1
1
0
1
0
0
1
0
Stuff
bit
5 bits in “1” in bitstream with stuffing bits

## Slide 87: Error Handling
Error Sources
  Format errors
    Invalid format, early end of frame, etc…
  Bit errors
    Actual bus level don’t correspond with the transmitted level
    Exceptions: during arbitration and in ACK field
  Bit-stuffing errors
    More than 5 bits with same level observed in the bus during Data or Remote Frame transmission

## Slide 88: Error Handling
Error Sources
  Acknowledge errors
    ACK bit is not asserted (dominant level) by any node subscribing node
    May indicate an actual error or that the transmitting node is “alone” in the network
  CRC errors
    CRC check fails (data corruption due to EMI, physical bus failures, etc.)

## Slide 89: Error Handling
CAN nodes have error counters
  Transmit error counter (TEC)
  Receive error counter (REC)

## Slide 90: Error Handling
Transmit error counter (TEC)
  Starts with value of zero upon initialization
  Min value is zero, max value is 255
  Increased when the node detects an error on the frame it is transmitting
    Typically, increased by 8 when detecting a TX error
  Decreased when the node successfully transmits a frame
    Decreased by 1

## Slide 91: Error Handling
Receive error counter (REC)
  Starts with value of zero upon initialization
  Min value is zero, max value is 255 (this value typically doesn’t exceed 135)
  Increased when the node detects an error on the frame it is receiving
    Increased by 8 when the node identifies the error by itself, increased by 1 otherwise
  Decreased when the node successfully receives a frame
    Decreased by 1

## Slide 92: Error Handling
Depending on the values of the Transmit and Receive error counters, the node can be in any of the following states:
  Error active state
    TEC < 128 and REC < 128
  Error passive state
    TEC ≥ 128 or REC ≥ 128
  Bus-off state
    TEC ≥ 255

## Slide 93: Error Handling
Error Active State
Error Passive State
Bus-Off
State
Normal Mode Request and
128 occurrence of 11 consecutive recessive bits
/ TEC = 0, REC = 0
TEC < 128 and
REC < 128
TEC ≥ 255
TEC ≥ 128 or
REC ≥ 128
Init
/ TEC = 0, REC = 0

## Slide 94: Error Handling
Error Active State
  Is the “normal” state to be if there are no abnormal errors in the network (TEC and REC values are “low”)
  In this state the node transmits and receives frames normally
  In this state, if a node detects an error, it informs the rest of the nodes in the bus by transmitting an active error frame

## Slide 95: Error Handling
Active Error Frame Format

## Slide 96: Error Handling
Active Error Frame Format
  Primary Error Flag: 6 dominant bits
    Explicitly violates bit-stuffing rule
    Other nodes in the network may generate further error frames due to the bit-stuffing violation
  Secondary Error Flag: From 0 to 6 bits (depending on subsequently generated error frames)

## Slide 97: Error Handling
Active Error Frame Format
  Publication of this frame abruptly interrupts current frame being transmitted
  Publishing node can retry transmission later

## Slide 98: Error Handling
Error Passive State
  This state indicates a problematic situation in the bus since the REC or TEC counters are relatively high
  Node stills transmits and receives frames, but, in the case of transmission, it “sabotages” itself by including additional 8 bits in the interframe space via the “suspend transmission” field.
     Other competing nodes will likely take the bus before since they don’t have those extra 8 bits in the interframe space.
  In this state, if a node detects an error, it transmits a passive error frame

## Slide 99: Error Handling
Passive Error Frame Format
  Passive Error Flag: 6 recessive bits
  Error delimiter: 8 recessive bits
  The passive error frame is “invisible” to the CAN bus
    Consists of only recessive bits
    Doesn’t disrupt any on-going communication

## Slide 100: Error Handling
Bus-Off State
  This state indicates a critical situation in the bus most likely caused by the node itself
  Node “disconnects” itself from the network
    No reception of frames
    No transmission of frames

## Slide 101: Error Handling
Bus-Off State
  Exit criteria from this state may imply (application specific):
    Waiting time
    Re-initialization of at least the CAN controller
    Wait for bus in idle for a given time (128 occurrences of 11 consecutive recessive bits)

## Slide 102: Contents
  CAN Overview
  Protocol Specification
      Physical Layer
      Data Frame Format
      Remote Frame Format
      Arbitration
      Bit Stuffing
      Error Handling
  Network Design
      Transmission Types
      Design Steps

## Slide 103: Transmission Types
Message Transmission Types
  Cyclic (most used)
  Spontaneous
  Cyclic and Spontaneous
  By-Active-Function (BAF)
Note: These transmission types are not part of the CAN specification but are defined at “application” level

## Slide 104: Transmission Types
Cyclic messages
  Are transmitted cyclically at a defined transmission period
  Examples of period values
    10ms to 50ms for critical highly-changing data messages
    100ms to 500ms for non-critical messages
    ≥1000ms for slowly-changing data messages

## Slide 105: Transmission Types
Cyclic messages

## Slide 106: Transmission Types
Cyclic messages
  For cyclic messages is common to define a timeout time to check for data availability
  This timeout time is often defined as a multiple of the message’s period time, examples:
    10 times its period
      A message with T=20ms will have timeout time of 200ms
      A message with T=100ms will have timeout time of 1000ms

## Slide 107: Transmission Types
Cyclic messages
  If a message is not received within its defined timeout time, the data is considered as not available.
    Application of receiver node needs to assume data values (for each signal) to use for its functional purposes.
    E.g., Use “last-known-value”, assume a fail-safe value by default, etc.

## Slide 108: Transmission Types
Spontaneous messages
  Transmitted only when the data of the message changes
     Conveyed signal changes
  No defined period
  A minimum separation time is defined
     e.g., 20ms

## Slide 109: Transmission Types
Spontaneous messages

## Slide 110: Transmission Types
Cyclic and Spontaneous messages
  Have a defined period for transmission but are also transmitted if there is a data change in between periodical instances
  Period needs to be defined
  A minimum separation time is defined
  Cyclic and spontaneous message instances need to be handled properly, e.g., to respect minimum separation time, etc.

## Slide 111: Transmission Types
Cyclic and Spontaneous messages

## Slide 112: Transmission Types
By-Active-Function
  Message transmission is associated to the occurrence of an “event”
  If the event hasn’t occurred or is not active, then there is NO message transmission
  If the event occurs or becomes active, then the messages start being transmitted with a defined period
  Message stops being transmitted if the event is no longer active or if certain number of transmissions have been executed

## Slide 113: Transmission Types
By-Active-Function

## Slide 114: Network Design
CAN Network is designed “offline”
Once defined, each nodes gets implemented according to their applicable messages/signals
Common formats to document a CAN network design
  Tables (e.g., MS Excel, LibreOffice Calc)
  DBC files (Vector proprietary format)
  ARXML files (AUTOSAR)

## Slide 115: Network Design
Basic steps for designing a CAN network
  Note: Steps shown here are not exhaustive, just an example. Some steps have dependencies from other steps, so the order mentioned here is not strict
  Define Network characteristics
    Bit-rate (according to data needs, wire length, etc.)
    Physical bus to use (single-wire, two-wire)

## Slide 116: Network Design
Basic steps for designing a CAN network
  Define Participant Nodes
    Node name
    Node description
    Map nodes to ECUs
       E.g., Gateway ECUs implement multiple nodes of different CAN networks

## Slide 117: Network Design
Basic steps for designing a CAN network
  Define Data Signals
    Signal Name
    Signal description
    Signal characteristics
      Length
      Unit, resolution, range, enumerated values, default value, etc.

## Slide 118: Network Design
Basic steps for designing a CAN network
  Define Network Messages
    Message Name
    Message description
    Message ID (lower value  higher priority)
    Message Format (standard, extended)
    Message transmission type (cyclic, spontaneous, etc.)

## Slide 119: Network Design
Basic steps for designing a CAN network
  Define Message Publisher and Subscriber(s)
    Which node will transmit the message?
    Which node or nodes will receive the message?
       Define timeout times for subscriber nodes if required

## Slide 120: Network Design
Basic steps for designing a CAN network
  Pack signals into messages
    Assign signals to messages
    Define signal layout within message:
      Starting Byte
      Starting Bit

## Slide 121: Questions & Answers
Thanks for your attention!
Questions, Comments?

## Slide 122: Bibliography
ISO 11898:2015, “Road vehicles — Controller area network (CAN)”, International Standards Organization, 2015
Online sources:
  https://elearning.vector.com/mod/page/view.php?id=333
  https://www.autovision-news.com/electrification/changes-vehicle-electrical-architecture/
  https://resources.altium.com/p/Controller-Area-Network-Bus-Introduction-and-History
  https://en.wikipedia.org/wiki/CAN_bus
  https://www.csselectronics.com/pages/can-bus-simple-intro-tutorial
  https://store.chipkin.com/articles/can-bus-protocol-page-2
  https://www.linkedin.com/pulse/hitchhikers-guide-hacking-connected-cars-ecus-alissa-valentina-knight/

## Slide 123: Bibliography
Stock images:
  https://www.freepik.com/free-photo/metallic-color-sport-car-bridge_5896016.htm#page=6&query=automotive&position=30&from_view=search&track=sph